## Slide 1
Experimental Aeroacoustics
Lecture 3.3
Propeller and Propfan Noise

## Slide 2
Module content
Propeller sources of noise
Harmonic, unsteady and random components
Harmonic noise prediction
Extension to contra-rotating propeller

## Slide 3
Learning objectives
Understand what the sources of propeller noise are
Be able to differentiate between thickness noise, loading noise and non-linearities
Understand the procedure to predict noise in multiple propellers
Sketch the procedure to predict noise in more complex configurations

## Slide 4
Introduction
Propellers are generally open (unshrouded) rotating bladed devices. They have been used extensively from the 1940’s for efficient propulsion.

## Slide 5
Introduction
The most important sources of noise for a propeller are:
Thickness noise → Volume displacement of the blades
Loading noise → Circumferential non-uniform loading (rotation)
Unsteady loading → Inflow angle or inaccuracies in the blade pitch
Quadrupole noise → Nonlinearities due to wake interaction
Broadband noise → Rotating boundary layer in blade edge
Installation noise → Interaction of wakes with surrounding structures

## Slide 6
Introduction
Aircraft applications, general configurations:
Single propellers:
Few straight narrow blades
High-performance → small velocity increase to large amount
Moderate flight speed and subsonic rotation regime
Propfan propulsion
High subsonic speed propellers
Increase in speed compensated by swept blades
Efficiency losses are compensated by number of blades
Counter-rotating propfan
High subsonic cruise speed
Recovering of swirl by second rotor/stator
Increase in noise due to slipstream interaction

## Slide 7
Propeller noise can be divided into:
Harmonic noise
Broadband noise
Narrow-band random noise
Harmonic noise
For a propeller running at N[rpm] with B blades:
    The fundamental frequency is NxB
    Blade passage is at 1/(NxB)
    Several harmonics are present
Broadband noise
All frequencies and characteristics, similar to TBL-TE noise
Narrow-band random noise
The energy is spread out in different frequencies
Still with a periodic footprint
Introduction

## Slide 8
Steady sources of noise
Steady sources are constant with respect to “an observer moving with the blade”
Linear thickness
Linear loading
(Non-linear) quadrupole
Linear thickness → monopole distribution, important at high speeds !!!
Transverse periodic displacement of the air by the volume of a passing element
Dependent to blade volume and airfoil shape:
Frequencies function of → blade cross-section
rotational speeds
Loading noise
Thrust and torque → important at moderate speeds, dipoles
Quadrupoles
At high speeds, especially at transonic and for swept blades, high-tip-speed propellers and helicopter rotors.

## Slide 9
Unsteady and random sources of noise
Unsteady sources are time dependent in “the rotating frame of reference of the blade”
Periodic and random variation of loading of the blades:
Inflow angle, seen as periodic change of angle of attack
Unsteady sources in the blades (blades pitch mismatch)
In contra-rotating propellers → interaction
Potential fields due to inlets or wings
Random sources of noise in propellers are sources of broadband noise:
Inflow turbulence and interaction with the blade
Turbulent boundary-layer trailing-edge noise

## Slide 10
Harmonic noise prediction
Farassat modified Ffowcs Williams and Hawkings equation to account for surfaces in motion in a fluid:
Wave operator on pressure p
Local velocity of the surface normal to it
i-component of the surface force
Dirac delta function
(x,y,z) = 0 surface equation
R force {.., li,..}
n(surf)
ω
vs
vt
vn
Contribution due to thickness noise
Contribution due to loading noise
General form

## Slide 11
Harmonic noise prediction
Contribution due to thickness noise → sources and sinks of strength q
Contribution due to loading → doublets associated with F vector
Blade section at angle of attack
x
x
x
Contribution of sources and sinks
Thickness noise
Noise footprint
Contribution due to loading
Vortical distribution
+
As previously explained the solution can be found in:
the time domain
the frequency domain

## Slide 12
Time solutions of the equation are listed by Farassat (1, 1A, 2, 3).
The most important formulations are listed in:
Aircraft Noise Prediction Program ANOPP
Farassat-Padula Advanced Turboprop Prediction (DFP-ATP)
The procedure of solution is similar to the one of FWH, by employing Green function in 3D space.
Harmonic noise prediction
Contribution consisting of two components: thickness and loading
Important parameters:
ret: retarded time
Mr: relative Mach number
c: speed of sound
Other formulations, example 1A isolate near and far-field contributions or account for supersonic effects (e.g. 3)

## Slide 13
Other solutions of the integral have been proposed by Hanson in the frequency domain employing Bessel functions for propagation of the single components.
Comparison with experimental data provided for the Gannet propeller (Rolls Royce)
Harmonic noise prediction

## Slide 14
Beside the different there is a huge difference between propellers in steady conditions and during flight.
Harmonic noise prediction
Magliozzi et al. 1977
Most of the non-uniformities get attenuated with some inflow speed
Directivity also plays a role

## Slide 15
The harmonic noise prediction can be extended to more complex configurations.
Example: Counter Rotating Propellers in pusher configuration (Jaouani et al. 2015)
Extension to contra rotating configurations
Observation
Isolated CRP → interaction noise by wake impingement, dominant component
Hp: viscous effects neglected
propagation effects neglected
We know how to calculate the contribution from a single rotor, how can we treat the interaction?

## Slide 16
Separation of the interactions:
Extension to contra rotating configurations
Wing wake
Interaction N1:
Rotor 1 wake
Rotor 1 wake
Interaction N2:
Rotor 2 wake
Interactions are split in considering the dominant effect of the wing wake on the upstream rotor.
The effect of the wing wake on the downstream rotor is considered minor.
Wing
Rotor 1
Rotor 2

## Slide 17
Extension to counter rotating configurations
Interaction N1:
Option 1
The wing → a propeller with one blade and ω = 0 [rad/s]
Advantage
The system wing/front-rotor can be seen as a doublet generating an interaction noise equivalent to N2 (rotor-rotor) interaction.
Disadvantage
The procedure predicts only the loading noise contribution.
Option 2
The wing is removed → its wake becomes a non-homogeneous inflow conditions
Hanson and Parzych formulation can be used, separating again between loading and thickness
noise.

## Slide 18
Extension to contra rotating configurations
Therefore the problem can be generalized by discussing the interaction between a downstream blade row and the flow generated by the upstream blade row
Upstream R1
Downstream R2
V∞
Step 1:
Distorted velocity field downstream of the first row
Step 2:
The distorted velocity generate an unsteady force on the downstream propeller
Chord-based element
Shape function
N.B. retarded time

## Slide 19
Extension to contra rotating configurations
Therefore the problem can be generalized by discussing the interaction between a downstream blade row and the flow generated by the upstream blade row
Upstream R1
Downstream R2
V∞
Step 3:
We can now use the acoustic pressure due to a moving point force FWH equation
= angle between observer and flight axis at time τ
Step 4:
The far field solution of the blade loading can be found by integration of dp in the far field.

## Slide 20
Extension to contra rotating configurations
Therefore the problem can be generalized by discussing the interaction between a downstream blade row and the flow generated by the upstream blade row
Upstream R1
Downstream R2
V∞
Step 5:
We still miss the contribution due to the impingement of the wakes of the first rotor on the second one.
The modelling is quite complicated and usually carried out with:
Prandtl’s Wake Model → u’~X-1/2
Schlichting Wake Model (wake width b) → prop. to CD (drag coeff.) and chord
Gaussian Wake Model → model for the velocity distribution, exponential form
The models are propagated as change in velocity again similarly to step 3!

## Slide 21
Experimental examples
Experimental overview, Vanderover and Visser:
Single Rotating Propeller SRP
Contra Rotating Propeller

## Slide 22
Experimental examples
Experimental overview, Vanderover and Visser:
Single Rotating Propeller SRP
Contra Rotating Propeller